## Slide 1: Digital twin for energy industry
Wind Turbine Modeling Workshop
Adrien Hirvoas, Ph.D. - FEM
ISEN Yncréa Ouest
January 16th-18th, 2023

## Slide 2: Wind Turbine Modeling Workshop - Agenda
Day 1: Welcome and Introductions Wind Turbine Modeling Overview Overview of OpenFAST Practical work: Installation Inputs and outputs workflow OpenFAST Modules OpenFAST tool: python-toolbox Practical work: Practicing Run your first simulation | Day 2: OpenFAST reminder OpenFAST tutorial Practical work: Floating Offshore Wind Turbine Post-Processing A digital twin approach Conclusion & Question

## Slide 3: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
Practice – Onshore wind turbine

## Slide 4: Welcome and Introductions
Myself in short
Personal Profile
Education
Contact info
Work Experience
Research engineer with a focus on mathematics applied to floating offshore wind turbine
Engineering Diploma in Mechanical Engineering
Master of Research
Ph.D. in applied Mathematics
7 years of R&D in wind turbine system
Research institutes: IFPEN / FEM
Adrien Hirvoas
LinkedIn: adrien-hirvoas
Email: adrien.hirvoas@france-energie-marines.org

## Slide 5: Welcome and Introductions
France Energies Marines (FEM) in short
French National Research Institute fully dedicated to Offshore Renewable Energies
Staff 70
Since 2012
€6M budget in 2021 100% allocated to R&D
Headquarters in Brest Offices in Le Havre, Nantes and Marseille
Institute supported by France 2030 investment plan

## Slide 6: Welcome and Introductions
FEM - Scientific and technological roadmap
SYSTEMS DESIGN AND MONITORING
Structure, mooring and electrical cable
Hydrodynamic and structural coupling
Digital twins and in-service monitoring
Technological innovation
4 cross-cutting and complementary R&D programmes
SITE CHARACTERISATION
Spatialisation of observations
Characterisation of sea states
Wind characterisation at sea
Climate change
Hydrosedimentary processes
ENVIRONMENTAL INTEGRATION
Effects on ecosystem compartments
Changing scale in terms of socio-ecosystem, space and time
Tools for environmental integration
FARM OPTIMISATION
Farm architecture
Grid integration (hydrogen...)
Installation, operation and maintenance

## Slide 7: Welcome and Introductions
About this workshop
  A GitHub repository is provided with some simulation folder and slides
  2 x 3 hours – 08/03/2023 and 13/03/2023
  Don’t hesitate to ask questions (even during the presentation)
  Objectives
    Clarify the concept of Wind Turbine Modeling
    Clarify the concept of Digital Twin
    Allow you to build your first wind turbine numerical model

## Slide 8: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
Practice – Onshore wind turbine

## Slide 9: Wind Turbine Modeling Overview
Wind Turbines are as Large as civil structures
but are active machines
Development of wind capacity
2001~2020

## Slide 10: Wind Turbine Modeling Overview
Fixed wind turbines
Floating wind turbines
Offshore wind turbines (still in development)

## Slide 11: Wind Turbine Modeling Overview
Why?
Lower wind cost of energy requires technology advancement through improved engineering capability founded on physics.
What?
Improved physics-based engineering design competence and software needed to advance wind energy technology.
How?
Use the knowledge, data, and results from broader wind research to improve physics-based engineering design competence and software.
Engineering Design Competence and Models
Physic-Based
Knowledge
Real-World
Data
Advanced Wind
Energy
Technology at
Lower Cost

## Slide 12: Wind Turbine Modeling Overview
Coupling Between Fluids, Structures, and Controls
Aerodynamics
Structures
Controls
Hydrodynamics

## Slide 13: Wind Turbine Modeling Overview
What is a Digital Twin ? (For you)
An online survey: https://forms.gle/QfxrfTnN2anhtUg7A
Possible responses:
A fully defined model, able to simulate the full behavior of an asset
A model similar to a real system that receives data from sensors on the real asset
A 3D model
Simulation of a manufacturing asset
A moving model
All of the above
I don’t know

## Slide 14: Wind Turbine Modeling Overview
Digital Twin - Wind Turbine
What for ?
Improve availability
Reduce operational expenditure (OPEX)
Streamline inspection
Anticipate life extension
Improve future designs

## Slide 15: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
Practice – Onshore wind turbine

## Slide 16: Overview of OpenFAST
OpenFAST: An Open-Source Tool for Wind Turbine Physics-Based Engineering Modeling
An open-source wind turbine physics-based engineering tool
Mathematical models are implemented in distinct modules & interconnected to solve for the global, coupled, dynamic response of a system
Currently an open-source code-development community for physics-based engineering models

## Slide 17: Overview of OpenFAST
OpenFAST - inputs and outputs
Main.out
Main*.sum
Main*.ech
…
vtk*/
Main*.lin
INPUTS:
one main file (extension .fst) which references other files
OUTPUTS:
one data file (.out or .outb) with time series of selected output channels
optional files: summary (.sum), echo (.ech), linearization (.lin), visualization (vtk)
Main.fst
ElastoDyn.dat
AeroDyn.dat
ED_Tower.dat
ED_Blade.dat
….
AD_Blade.dat
Polar.dat
Time (s) | Rotor Speed (rpm) | … | Channel[n] (unit)
0 | 5.0 |  | 
0.1 | 4.9 |  | 
… | … |  | 
tMax | 5.5 |  | 
OpenFAST executable

## Slide 18: Overview of OpenFAST
INPUTS
OUTPUT
Typical folder:
EXE
OpenFAST - inputs and outputs (in practice)

## Slide 19: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
Practice – Onshore wind turbine

## Slide 20: OpenFAST modules
Primary (.dat)
ElastoDyn | Structural dynamics
Primary (.dat)
AeroDyn | Aerodynamics
Primary (.dat)
InflowWind |
Wind Inflow
Primary (.dat)
ServoDyn |Control and Electrical Drive Dynamics
Primary (.dat)
HydroDyn |Hydrodynamics
Primary (.dat)
MAP++ |Quasi static Mooring Dynamics
OpenFAST driver
Primary (.fst)
Additional ElastoDyn input files (.dat)
Additional AeroDyn input files (.dat)
Wind data files (.wnd, .bts, hh, etc…)
Bladed-style external controller (.dll)
Additional HydroDyn input files (.dat)
Times Series (.out, .outb)
Linearization (.lin)
Visualization (.vtp)

## Slide 21: OpenFAST modules
ElastoDyn
  Computes structural response as part of the aero-hydro-servo-elastic solution
    Combined modal & multi-body representation through 24 Degrees of Freedom
      Multi-body: platform, nacelle, generator, gears, hub, tail
      Modal: blades, tower
    Blade & tower modeling assumptions:
      Bernoulli-Euler beams
      Straight & isotropic
      Bending only
      Small to moderate deflections
Modal
representation

## Slide 22: OpenFAST modules
AeroDyn
  Computes aerodynamics (lift, drag, pitch) as part of the aero-elastic solution
    Wind-inflow input:
      Uniform, unsteady
      Turbulent (TurbSim)
    Wake modeling:
      Blade Element Momentum (BEM) theory
      Dynamic wake (DBEMT)
      Dynamic stall modeling:
      Beddoes-Leishman (semi-empirical)
      Tower drag & influence on wind
Schematic representing an annular actuator in BEM theory from [8]

## Slide 23: OpenFAST modules
InflowWind
  Undisturbed wind inflow:
    Steady
    Uniform, but time-varying, e.g., deterministic gusts from IEC (IECWind)
    Full-field (FF) turbulence (TurbSim, Mann)
    User-defined

## Slide 24: OpenFAST modules
ServoDyn
  Control and Electrical Drive Dynamics
    Modeling: standard conventional pitch controller
      Two main operating regimes:
        Maximum Power Regime
        Constant Power Regime
  Floating context: problems due to negative damping

## Slide 25: OpenFAST modules
HydroDyn
  Computes wave-kinematics & hydrodynamics as part of the hydro-elastic solution
    Waves & Current
      Wave kinematics:
        Linear regular (periodic)
        Linear irregular (stochastic):
      Wave direction & directional spreading
    Steady sea currents:
      IEC-style sub-surface, near surface, & depth-independent
      Or user-defined
    Hydrodynamic Loading
      Strip theory (Morison)
      Potential flow (WAMIT):
        1st and 2nd-order (QTF or Newman’s approximation) theory
      Hybrid combination of these two
Multi-Directional Sea State
IEC Sea Currents

## Slide 26: OpenFAST modules
MAP++
  Quasi static
  Multi-segmented array of taut or catenary lines
  Elastic stretching
  Apparent weight of lines
  Clump weights & buoyancy tanks
  Seabed friction
  Nonlinear geometric
Constraint States:
Displacements
Velocities
Parameters:
Line properties
Line connectivity
Gravity
Inputs:
Platform displacements
Outputs:
Line tensions
Line displacements
MAP++ module

## Slide 27: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
Practice – Offshore wind turbine

## Slide 28: Practice – Offshore wind turbine – Google Colab
What is Google Colab?
  Google Colab which stands for Google Colaboratory is a cloud platform
  provided by Google to run Python Notebook’s without need to install
  anything on your local machine.
Features of Google Colab
  Zero Setup Required
  Free GPU Access
  Pre-installed Libraries
Accessing Google Colab
  https://github.com/Ahirvoas/Training-Day1/blob/main/Tutorial_day1.ipynb

## Slide 29: Annex

## Slide 30: Annex – Local Installation
Prerequisites
The open-source Python distribution platform ANACONDA
  To download the individual edition: click here
Installation
Windows | macOS | Linux
Use the precompiled executable named openfast_x64.exe in the shared folder Test by opening a command prompt, moving into the directory containing the executable, and running a simple test command: | Conda Installation Open an anaconda prompt command Install OpenFAST in a new environment | 
cd path\to\folder
openfast_x64.exe /h
# conda create a new environment
conda create -- clone base –n openfast_env
Conda activate openfast_env
# install OpenFAST through the conda channel
conda install –c conda-forge openfast==2.0.0
# Test OpenFAST
which openfast

## Slide 31: Annex – Local Installation
Let’s practice – installation
Windows | macOS | Linux
Use the precompiled executable named openfast_x64.exe in the shared folder Test by opening a command prompt, moving into the directory containing the executable, and running a simple test command: | Conda Installation Open an anaconda prompt command Install OpenFAST in a new environment | 
cd path\to\folder
openfast_x64.exe /h
# conda create a new environment
conda create -- clone base –n openfast_env
Conda activate openfast_env
# install OpenFAST through the conda channel
conda install –c conda-forge openfast==2.0.0
# Test OpenFAST
which openfast

## Slide 32: Annex – Local Installation
python-toolbox
Tools to read/write, preprocess and postproces OpenFAST files
  https://github.com/OpenFAST/python-toolbox
  As much as possible independent of OpenFAST version
  Installation:
    git clone http://github.com/OpenFAST/python-toolbox (or download the GitHub repository)
    conda activate openfast_env
    cd python-toolbox
    python -m pip install –e .