## Slide 1: Digital twin for energy industry
Wind Turbine Modeling Workshop
Adrien Hirvoas, Ph.D. - FEM
ISEN Yncréa Ouest
March 8th-13th, 2023

## Slide 2: Wind Turbine Modeling Workshop - Agenda
Day 1: Welcome and Introductions Wind Turbine Modeling Overview Overview of OpenFAST Practical work: Installation Inputs and outputs workflow Running OpenFAST OpenFAST Modules OpenFAST tool: python-toolbox Practical work: Installation Practicing Run your first simulation | Day 2: OpenFAST reminder OpenFAST tutorial Practical work: Floating Offshore Wind Turbine Post-Processing A digital twin approach Conclusion & Question

## Slide 3: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
OpenFAST tool: python-toolbox

## Slide 4: Welcome and Introductions
Myself in short
Personal Profile
Education
Contact info
Work Experience
Reasearch engineer with a focus on mathematics applied to floating offshore wind turbine
Engineering Diploma in Mechanical Engineering
Master of Research
Ph.D. in applied Mathematics
6 years of R&D in wind turbine system
Research institutes: IFPEN / FEM
Adrien Hirvoas
LinkedIn: adrien-hirvoas
Email: adrien.hirvoas@france-energie-marines.org

## Slide 5: Welcome and Introductions
France Energies Marines (FEM) in short
French National Research Institute fully dedicated to Offshore Renewable Energies
Staff 70
Since 2012
€6M budget in 2021 100% allocated to R&D
Headquarters in Brest Offices in Le Havre, Nantes and Marseille
Institute supported by France 2030 investment plan

## Slide 6: Welcome and Introductions
FEM - Scientific and technological roadmap
SYSTEMS DESIGN AND MONITORING
Structure, mooring and electrical cable
Hydrodynamic and structural coupling
Digital twins and in-service monitoring
Technological innovation
4 cross-cutting and complementary R&D programmes
SITE CHARACTERISATION
Spatialisation of observations
Characterisation of sea states
Wind characterisation at sea
Climate change
Hydrosedimentary processes
ENVIRONMENTAL INTEGRATION
Effects on ecosystem compartments
Changing scale in terms of socio-ecosystem, space and time
Tools for environmental integration
FARM OPTIMISATION
Farm architecture
Grid integration (hydrogen...)
Installation, operation and maintenance

## Slide 7: Welcome and Introductions
About this workshop
  A shared folder is provided with some simulation folder, Jupyter notebook tutorials and slides
  2 x 3 hours – 08/03/2023 and 13/03/2023
  Don’t hesitate to ask questions (even during the presentation)
  2 teams during the tutorials (Linux-MAC vs. Windows)
  Objectives
    Clarify the concept of Wind Turbine Modeling
    Clarify the concept of Digital Twin
    Allow you to build your first wind turbine numerical model

## Slide 8: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
OpenFAST tool: python-toolbox

## Slide 9: Wind Turbine Modeling Overview
Wind Turbines are as Large as civil structures but are active machines

## Slide 10: Wind Turbine Modeling Overview
Fixed wind turbines
Floating wind turbines
Offshore wind turbines (still in development)

## Slide 11: Wind Turbine Modeling Overview
Why?
Lower wind cost of energy requires technology advancement through improved engineering capability founded on physics.
What?
Improved physics-based engineering design competence and software needed to advance wind energy technology.
How?
Use the knowledge, data, and results from broader wind research to improve physics-based engineering design competence and software.
Engineering Design Competence and Models
Physic-Based
Knowledge
Real-World
Data
Advanced Wind
Energy
Technology at
Lower Cost

## Slide 12: Wind Turbine Modeling Overview
Coupling Between Fluids, Structures, and Controls
Aerodynamics
Structures
Controls
Hydrodynamics

## Slide 13: Wind Turbine Modeling Overview
What is a Digital Twin ? (For you)
An online survey: https://forms.gle/QfxrfTnN2anhtUg7A
Possible responses:
A fully defined model, able to simulate the full behavior of an asset
A model similar to a real system that receives data from sensors on the real asset
A 3D model
Simulation of a manufacturing asset
A moving model
All of the above
I don’t know

## Slide 14: Wind Turbine Modeling Overview
Digital Twin - Wind Turbine
What for ?
Improve availability
Reduce operational expenditure (OPEX)
Streamline inspection
Anticipate life extension
Improve future designs

## Slide 15: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
OpenFAST tool: python-toolbox

## Slide 16: Overview of OpenFAST
OpenFAST: An Open-Source Tool for Wind Turbine Physics-Based Engineering Modeling
An open-source wind turbine physics-based engineering tool
Mathematical models are implemented in distinct modules & interconnected to solve for the global, coupled, dynamic response of a system
Currently an open-source code-development community for physics-based engineering models

## Slide 17: Overview of OpenFAST
OpenFAST - inputs and outputs
Inputs
One main file (extension .fst) which references other files
Inputs
One data file (.out or .outb) with time series of selected output channels
Optional files: summary (.sum), echo (.ech), linearization (.lin), visualization (vtk)

## Slide 18: Overview of OpenFAST
Let’s practice – Prerequisites
The open-source Python distribution platform ANACONDA
  To download the individual edition: click here
Download and extract/save in an accessible local folder the attached compressed file:

## Slide 19: Overview of OpenFAST
Let’s practice – installation
Windows | macOS | Linux
Use the precompiled executable named openfast_x64.exe in the shared folder Test by opening a command prompt, moving into the directory containing the executable, and running a simple test command: | Conda Installation Open an anaconda prompt command Install OpenFAST in a new environment | 
cd path\to\folder
openfast_x64.exe /h
# conda create a new environment
conda create -- clone base –n openfast_env
Conda activate openfast_env
# install OpenFAST through the conda channel
conda install –c conda-forge openfast==2.0.0
# Test OpenFAST
which openfast

## Slide 20: Overview of OpenFAST
Let’s practice
Inputs and outputs (in practice) – Typical folder: 00_OnshoreSteadyWindCtrl
Running OpenFAST
Windows | macOS | Linux
Open a terminal/command line Navigate to the folder where the OpenFAST executable is: Call the OpenFAST executable with the main input file as argument: | Open an Anaconda prompt Activate the environment with OpenFAST Call the OpenFAST command with the main input file as argument: | 
cd path\to\OnshoreStead
openfast_x64.exe
conda activate openfast_env
openfast /h

## Slide 21: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
OpenFAST tool: python-toolbox

## Slide 22: OpenFAST modules
Primary (.dat)
ElastoDyn | Structural dynamics
Primary (.dat)
AeroDyn | Aerodynamics
Primary (.dat)
InflowWind |
Wind Inflow
Primary (.dat)
ServoDyn |Control and Electrical Drive Dynamics
Primary (.dat)
HydroDyn |Hydrodynamics
Primary (.dat)
MAP++ |Quasi static Mooring Dynamics
OpenFAST driver
Primary (.fst)
Additional ElastoDyn input files (.dat)
Additional AeroDyn input files (.dat)
Wind data files (.wnd, .bts, hh, etc…)
Bladed-style external controller (.dll)
Additional HydroDyn input files (.dat)
Times Series (.out, .outb)
Linearization (.lin)
Visualization (.vtp)

## Slide 23: OpenFAST modules
ElastoDyn
  Computes structural response as part of the aero-hydro-servo-elastic solution
    Combined modal & multi-body representation through 24 Degrees of Freedom
      Multi-body: platform, nacelle, generator, gears, hub, tail
      Modal: blades, tower
    Blade & tower modeling assumptions:
      Bernoulli-Euler beams
      Straight & isotropic
      Bending only
      Small to moderate deflections
Modal
representation

## Slide 24: OpenFAST modules
AeroDyn
  Computes aerodynamics (lift, drag, pitch) as part of the aero-elastic solution
    Wind-inflow input:
      Uniform, unsteady
      Turbulent (TurbSim)
    Wake modeling:
      Blade Element Momentum (BEM) theory
      Dynamic wake (DBEMT)
      Dynamic stall modeling:
      Beddoes-Leishman (semi-empirical)
      Tower drag & influence on wind
Schematic representing an annular actuator in BEM theory from [8]

## Slide 25: OpenFAST modules
InflowWind
  Undisturbed wind inflow:
    Steady
    Uniform, but time-varying, e.g., deterministic gusts from IEC (IECWind)
    Full-field (FF) turbulence (TurbSim, Mann)
    User-defined

## Slide 26: OpenFAST modules
ServoDyn
  Control and Electrical Drive Dynamics
    Modeling: standard conventional pitch controller
      Two main operating regimes:
        Maximum Power Regime
        Constant Power Regime
  Floating context: problems due to negative damping

## Slide 27: OpenFAST modules
HydroDyn
  Computes wave-kinematics & hydrodynamics as part of the hydro-elastic solution
    Waves & Current
      Wave kinematics:
        Linear regular (periodic)
        Linear irregular (stochastic):
      Wave direction & directional spreading
    Steady sea currents:
      IEC-style sub-surface, near surface, & depth-independent
      Or user-defined
    Hydrodynamic Loading
      Strip theory (Morison)
      Potential flow (WAMIT):
        1st and 2nd-order (QTF or Newman’s approximation) theory
      Hybrid combination of these two
Multi-Directional Sea State
IEC Sea Currents

## Slide 28: OpenFAST modules
MAP++
  Quasi static
  Multi-segmented array of taut or catenary lines
  Elastic stretching
  Apparent weight of lines
  Clump weights & buoyancy tanks
  Seabed friction
  Nonlinear geometric
Constraint States:
Displacements
Velocities
Parameters:
Line properties
Line connectivity
Gravity
Inputs:
Platform displacements
Outputs:
Line tensions
Line displacements
MAP++ module

## Slide 29: Day 1 - Agenda
Welcome and Introductions
Wind Turbine Modeling Overview
Overview of OpenFAST
OpenFAST modules
OpenFAST tool: python-toolbox

## Slide 30: OpenFAST tool: python-toolbox
Tools to read/write, preprocess and postproces OpenFAST files
  https://github.com/OpenFAST/python-toolbox
  As much as possible independent of OpenFAST version
  Installation:
    git clone http://github.com/OpenFAST/python-toolbox (or download the GitHub repository)
    conda activate openfast_env
    cd python-toolbox
    python -m pip install –e .
Let’s practice using Jupyter Notebook !
  Case – Onshore turbine steady wind with simple controller